## Slide 1: CBR in the Oil Industry
Dustin Dannenhauer
dtd212@lehigh.edu
Presentation for CSE 435
11/05/2012

## Slide 2: Contents
Oil Industry
Drilling for Oil
Problems
Overview of Using AI
TrollCreek
Drill Edge

## Slide 3: Oil Industry

## Slide 4: The Oil Industry
Oil and gas main energy sources in many countries
New wells are continuously demanded
Currently about 1190 offshore rigs in the world, %70 operational at any time
Over 3000 rotary land rigs in the world (2000 in US alone)
2025 forecasts an estimated need of 115 million BOPD from 85 million in 2010 (McCormack 2010)
Industry is heavily technology dependent
Notes: 30 seconds

## Slide 5: Oil Industry
Goals:
  Measurable return on investment
  Reduction in accidents (fires, blowouts, sinking/capsizing)
  Improvement in oil and gas measurement yield
  Fewer lost days of production
CBR can address all of these

## Slide 6: Drilling for Oil

## Slide 7: Drilling for Oil
Educational Video:
http://www.ustream.tv/recorded/8990220
http://www.youtube.com/watch?v=Q9gGqNUxQ5Q
Tripping: act of pulling drill string out and feeding it back in
Notes: 3 minutes for video – highlight important parts of the process

## Slide 8: Process of Drilling
Complex Operation
Symptoms/Problems generally arise around the drill bit
Each well may experience similar and new problems
  Especially given trajectories and composition
The source of oil may be as far as 10 km away from drilling rig [3]
Notes: 1 minute

## Slide 9: Example: Deviated and Horizontal Drilling

## Slide 10: Problems

## Slide 11: Specific Problems to Drilling
Hole Cleaning
Hole Collapse
Swelling
Erosion of Weakened Wellbore
Thick Filter Cake
Lost Circulation (TrollCreek)
Dissolving

## Slide 12: Problems w/ Knowledge in Industry
“Experience Attrition”
  Not just age gap – communication gap (soft and hard skills)
Want “Lessons Learned” and “Best Practices
  Study (Brett et al., 98) showed benefit of ~10% with sharing best practices within a company
Real Time Operation Centers
  Good but still not perfect
    Engineers staring at graphs 12 hours straight
    Loss of communication between shifts

## Slide 13: Overview of Using A.I.

## Slide 14: Why Use CBR/A.I. in Oil Industry
Reduce costs (reduce non-productive time, NPT)
  Offshore rigs cost hundreds of thousands of dollars per day per rig
  NPT up to 30%
  If NPT reduced 5% in a year, savings of 2.1 Billion
  Offshore drilling typically takes 1 month high investment
Increase safety
Anything that can improve the process is demanded
Address Knowledge Problems
  Limited access to human experts
  Age gap problem
Notes: 3-5 minutes

## Slide 15: General Sources of Data
Sensors installed at surface and downhole(@ drillbit)
Data is transmitted and translated
  Generally monitored by humans reading real-time parameter graphs
  Huge amount of data
  Keeping live physical models is computationally expensive
  Sometimes requires manual computation
Documents:
  Daily drilling reports
  End of well reports for every single well
Human Engineers

## Slide 16: Why machine learning doesn’t work
Could not predict problems directly
Very few serious examples
  Stuck pipe, stuck drill string, etc may only happen few times a year
  Necessary to learn from very few examples
While generally not more than 10-20 parameters, often not possible to detect symptoms without looking at trends and frequencies over the last 12-24 hours
Machine learning is still used – but not as primary technique

## Slide 17: Problems with Knowledge
Knowledge loss from poor communication, between shifts, etc leading to late identification of a problem
  Some engineers stare at graphs 12 hours straight
Just becoming aware of a situation is crucial
Example problems:
  Drilling pipe gets stuck in the ground because gravel pack around it
  Drillstring twists off and drilling mud is lost in the formation

## Slide 18: TrollCreek [4]
  Skalle and Aamodt, 2005

## Slide 19: TrollCreek
Address all phases of drilling process:
  Planning (TC addresses drilling engineer)
  Plan Implementation (TC addresses the driller and platform superintendent)
  Post Analyses (adding the drilling engineer and management)
Cases describe specific situations
Indexed by relevant features
Structured into subcases at several levels
They are indexed by direct, non-hierarchical indices, leaving indirect indexing mechanisms to be take care of by the embedding of the indices with the general domain model

## Slide 20: TrollCreek
All cases contain knowledge of:
  Identifying information – such as owner, place/date, formation/geology, well section, depth/mudtype
  Recorded parameter, specific errors or failures
  Necessary procedures to solve the problem, normative cases, best practice, repair path (row of events)
  Final path, success ratio of solved case, lessons learned, frequently applied links
    Links may go to such things like corporate databases
    For example: logging and measurement databases
    or textual lessons learned documents or formal drilling reports

## Slide 21: TrollCreek
Initial case matching using standard weighted feature sim metric
Each case in this set is either extended or reduced, based on explanations generated within the general domain model
Cases are structured in such a way that makes them suitable for finding the solution of a problem and/or to search for missing knowledge

## Slide 22: TrollCreek
An initial repair path is always tried out by the drilling engineer, which usual succeeds.
However, if it fails, it turns into a new case, or new problem.
The model based reasoning with the general domain model may find a solution, even if no case is found. Then this specific situation, with this new solution, gets stored as a new case transforming general domain knowledge combined with case-specific data, into case-specific knowledge

## Slide 26: DrillEdge [3]

## Slide 27: DrillEdge
Real-Time Decision Support System
High Cost Oil-Well Drilling Operations
Developed by Verdande Technology (Norway)
Awarded Meritous Award for Engineering Excellence for DrillEdge by E&P Magazine
Cost about 4.5 million to reach first commercial version in 2009
Currently 12 full time developers
Deployed on over 200 wells

## Slide 28: DrillEdge: Purpose
Predict Problems
Classify different kinds of situations
Give advice how to mitigate problems

## Slide 29: DrillEdge: Cases
Two parts: Description and Solution
  Description used to compare cases
  Solution is an experience transfer from human to human
Cases are captured and written by drilling experts
Represented as tree structures in XML files

## Slide 30: DrillEdge: Case Descriptions
Features, such as:
  Symptoms (location and time)
  Design of bottom hole assembly
  Qualities of formation or its composition
  Type of drilling fluid and or composition
  Trajectory of the well
Notes: 3-5 minutes - Be sure to go into detail about each one of these – also make sure you put effects so that as you click each example pops up

## Slide 31: DrillEdge: Case Solution
Textual description intended for humans (4 parts)
Problem description part
  Describes the specific situation
Symptoms part
  Describes the symptoms they were experiencing
Response action
  Actual actions taken
Recommended action
  Based on post-analysis – what should have been done
Notes: 1-2 minutes – just let class read slide

## Slide 32: DrillEdge: Cases as XML Files
Root node has two main sections:
  Problem description
  Problem solution
  Each of these may contain other sections or leaf nodes
Example:
  Problem Description contains:
    Formation
    Drilling fluid
    Bottom hole assembly
    Well Geometery
    Symptoms
Formation section contains formation name and composition (lithology)
Drilling fluid section contains properties describing the fluid, such as mud weight and whether oil or water based

## Slide 33: DrillEdge: Sequence Section of Case Description
Special kind of feature: Sequence Section
Contains “events” (which are symptoms)
Different types depending on type of symptom representing
Two sequence sections:
  Distribution of events over a given depth of where the drill bit is
  Represents events over a limited time period

## Slide 34: DrillEdge: Case Similarity
Compare root nodes
Similarities of root nodes are aggregated into section similarities
Section similarities are combined recursively until the similarity of the root nodes are found
Root nodes can be of different types (ints, doubles, enumerations, sequences).
Different similarity measure can be configured for each comparison
Some are standard, others domain specific

## Slide 35: DrillEdge: CBR Cycle
Gunderson, Aamodt, & Skalle (AAAI 2012)

## Slide 36: DrillEdge: Overall Process
Continuously compares the current situation with cases in case base
Each time step, real-time data is interpreted
If symptoms of problems are identified, events are fired
Current situation is represented by both important events and contextual information
Events are stored in the case as depth and time sequences

## Slide 37: DrillEdge: From Engineer’s Perspective
DrillEdge searches and retrieves cases and compares them to the current case
Sorted on similarity
All past cases above a given threshold are visualized on a GUI element, a radar, to alert and advice the user of past historic cases
New case is created if current situation is not covered by any cases stored in the case base or if other advice applies to this situation
New cases are quality assured through peer review by a group of experts

## Slide 39: DrillEdge: Challenges
3 Main Challenges:
Revising symptom recognition
Time used to find and capture a proper case
Real-time demands on similarity comparison

## Slide 40: Summary and Questions?
Drilling for oil is a complex operation
Access to data and information is a huge problem in oil industry
CBR integrated with different reasoning methods has proven to be effective in reducing NPT

## Slide 41: References
[1] Shokouhi, S. V., Aamodt, A., & Skalle, P. (2010). Applications of CBR in oil well drilling. In Proceedings of 6th International Conference on Intelligent Information Processing (pp. 102-111).
[2] Pål Skalle, Agnar Aamodt and Odd Erik Gunderson Transfer of experience for improved oil well drilling Advances in Drilling Technology - E-proceedings of the First International Conference on Drilling Technology (ICDT - 2010)
[3] Gundersen, Odd Erik, et al. "A Real-Time Decision Support System for High Cost Oil-Well Drilling Operations." Innovative Applications of Artificial Intelligence, IAAI (to appear, 2012) (2012).
[4] Skalle, Pål, and Agnar Aamodt. "Knowledge-based decision support in oil well drilling." Intelligent Information Processing II (2005): 443-455.
[5] Shokouhi, Samad, et al. "Determining root causes of drilling problems by combining cases and general knowledge." Case-Based Reasoning Research and Development (2009): 509-523.

## Slide 42: Timeline of CBR Systems
Irrgang et al. (1999)
  CSIRO – CBR for well planning – started “Drilling Club”
Skalle et al. (2000) (KI)
  CBR during drilling - w/ 50 cases from North Sea – lost circulation
Bhushan et al. (2002)
  CBR to globally search for reservoir analogues for planning and development of oil fields
Mendes et al. (2003)
  CBR in Well Design – Initiative to model petroleum well design
  Fuzzy sets and genetic algorithms
Karvis and Irrgang (2005)
  Genesis – CBR for oil field design – multi-level indexing scheme
Khajotia et al. (2007)
  Non typical approach – CBR within predictive mathematical model

## Slide 43: CBR Systems
Irrgang et al. (1999)
  CSIRO – CBR for well planning – started “Drilling Club”
Skalle et al. (2000)
  CBR during drilling - w/ 50 cases from North Sea – lost circulation
Bhushan et al. (2002)
  CBR to globally search for reservoir analogues for planning and development of oil fields
Mendes et al. (2003)
  CBR in Well Design – Initiative to model petroleum well design
  Fuzzy sets and genetic algorithms
Karvis and Irrgang (2005)
  Genesis – CBR for oil field design – multi-level indexing scheme

## Slide 44: Ki-CBR Systems

## Slide 45: Knowledge Intensive CBR (Ki-CBR)
Skalle et al. (2000)
  CBR during drilling - w/ 50 cases from North Sea – lost circulation
Transfer of Experience
  Skalle, Aamodt, Gunderson 2010
TrollCreek
  Skalle and Aamodt, 2005
Mendes et al. (<insert year here>)

## Slide 46: Skalle et al. (2000) – CBR – North Sea - LC
Offshore oil well drilling
Focused on Lost Circulation
  Losing drill fluid in formation – fluid not returning to surface
  Many different solutions based on formation, fluid, and current technologies (cement, etc)
Extensive General Knowledge Model
50 different cases created from one North Sea operator
Retrieve 5 top cases
Informal evaluation showed the 2 best fitting cases gave valuable advice to the operator

## Slide 47: Skalle et al. (2000) – Cases & GKM
Case represents a user experience
Different attributes may match/not match by related with general knowledge model
General Knowledge Model supports by:
  Enables semantic searching for past cases (instead of pure syntactic) – 2 parameters that may seem different might be similar (for example may be different values but both are increasing)
  Help explain how past solution can help current situation (adaptation)
  Used to explain what to retain in new case (i.e. the ML part)

## Slide 48: Skalle et al. (2000) – Overall Process
a) Gather data
b) Detect a possibly approaching problem
c) Decide if gathered data are sufficient to define the situation as a new problem. If not;
d) Perform additional examinations (i.e. check loss rate, check circ. pressure etc.).
e) Search the case base for similar past cases.
f) Generate a set of the most likely hypothesis and present a set of possible solutions in descending order to the current problem.
g) Use general domain knowledge to provide explanatory support for each plausible
hypothesis, and refine the hypothesis list.
h) Interact with user to select the best hypothesis. Generate a detailed "to-do" list,
i) After the case has been solved, the case base can be updated based on the situation just experienced.

## Slide 49: CBR in Oil Industry
Cases generally describe abnormal situations
Some cases are normal situations similar to abnormal to help distinguish what makes a situation abnormal

## Slide 50: CBR Systems in the Oil Industry
Several researchers and companies have tried out CBR for oil drilling assistance, few reach deployment
CSIRO -> Genesis:
Mendes et al. : Formal Oil Well Planning Methodology
DrillEdge:
  only system that links on-line data streams to past cases for real-time decision support
Related domains: well planning, reservoir engineering, petroleum geology

## Slide 51: CSIRO -> Genesis
CSIRO -> Genesis
  One of the first
  Each well was represented as 1 case
  Case structure had three levels
    Groups of cases
    Groups of attributes
    Groups of defined drilling phases and operations
  Used multiple cases at varying levels of generality
  Used automated tools to:
    Extract knowledge
    Indexes for the case base from text description

## Slide 52: Mendes et al.
CBR in offshore well design (planning)
Resulted in a formalization of a methodology for planning an oil well in CBR context
Used fuzzy set theory for indexing and matching of index features
Genetic algorithm to determine the proper trajectory and all pertinent information for drilling

## Slide 53: KiCBR applied to Hole Cleaning
Hole Cleaning is one of the most important problems
  Continuous process
Extreme situations can cause well failure
Phenomenon is not completely understood
  Especially with deviated and horizontal drilling
Shokouhi, Aamodt, Skalle, Sormo (2009)

## Slide 54: KiCBR: Hole Cleaning
Why CBR?
  Allows us to view a large set of parameters as a single unit
  Previous studies only focused on one paramter at a time
Goal: Reduce Non Productive Downtime (NPT)
Real Time data is main source of problem description
Predict possible problems ahead of drill bit

## Slide 55: KiCBR: Hole Cleaning
Three knowledge models needed:
  Taxonomy – extracting important terms from domain
  Causal Model – model that describes causes and effects
  Case base
Features:
  Administrative Data, wellbore formation characteristics
  Plan data, static and variable drilling data
  Drilling activity before case occurence, response action
  Conclusion

## Slide 56: Case Structure

## Slide 57: Similarity Metric

## Slide 58: KiCBR: Sim Metric Explained
Relevance Factor is a numerical weight of a feature
Symbolic term only used with model based part
Three types of Features:
  Direct Observations – Inferred Paramters –Interpreted Events
  0.25 0.5 1.0

## Slide 59: KiCBR: Model

## Slide 60: Example Event: Pack Off
Notes: Another example of why ML doesn’t work

## Slide 61: KiCBR: Experiments
Leave-one-out cross validation
7 Cases
Using general knowledge (model) 2 benefits:
  Increase similarity
  May change which case is most similar

## Slide 62: Additional Information